## Slide 2: Light electric truck (18 tonnes) with a daily mileage of 150 km with 120 kW drive power from electric motor.
Battery Storage Systems SS 22

## Slide 3: Agenda
Introduction
Battery Technology Selection
Battery Cell Selection and Pack Design
Battery Management System and Cooling System
Load Profile Estimation
Ageing
Cost Analysis
Conclusion

## Slide 4: Introduction
Source : https://www.researchgate.net/publication/336687173

## Slide 5: Battery Technology
Criteria for choosing the battery technology for full-hybrid vehicles:
Gravimetric and volumetric power density
Gravimetric and volumetric energy density
Energy efficiency
Calendar lifetime
Cylce lifetime
Costs
Considered Technologies:
Lead-acid (Pb)
Nickel-cadmium (NiCd)
Nickel-metal hydride (NiMH)
Lithium-ion (Li-ion)
Sodium-nickel chloride (NaNiCl2)

## Slide 6: Battery Technologies – Volumetric Energy Density
Technology | Volumetric Energy Density
Lead-acid (Pb) | --
Nickel-cadmium (NiCd) | -
Nickel-metal hydride (NiMH) | o
Lithium-ion (Li-ion) | +
Sodium-nickel chloride (NaNiCl2) | +
Volumetric Energy Density1
1: https://upload.wikimedia.org/wikipedia/commons/c/c9/Secondary_cell_energy_density.svg

## Slide 7: Battery Technologies – Gravimetric Power- and Energy Density
Technology | Theoretical Minimum Weight for 70 kW Power and 1 kWh Capacity | Critical Factor
Lead Acid | 200 kg | Power
NiCd | 70 kg | Power
NiMH | 37 kg | Power
Lithium Ion | 14 kg | Energy
NaNiCl2 | 460 kg | Power
For most technologies, the gravimetric power density is more critical for the given application
: Considered Point for this application:
Gravimetric Energy-and Power Density1
1: Budde-Meiwes, Heide & Drillkens, Julia & Lunz, Benedikt & Muennix, Jens & Lehner (maiden name Rothgang), Susanne & Kowal, Julia & Sauer, Dirk. (2013). A review of current automotive battery technology and future prospects. Proceedings of the Institution of Mechanical Engineers, Part D: Journal of Automobile Engineering. 227. 761-776. 10.1177/0954407013485567

## Slide 8: Battery Technologies – Overview
Technology | Efficiency[1][2][3] | Lifetime | Costs | Power Density | Energy Density | Safety | other
Lead Acid | ~ 85 % | - | ++ | - | -- | + | Highest recycling quotes of all technologies (>95 %)
NiCd | 70 % - 85 % | + | - | o | - | - | Mature technology
NiMH | 70 % - 80 % | + | - | + | o | o | Poor deep-temperature performance
Lithium Ion | 85 % - 98 % | ++ | - | ++ | ++ | o | Do not offer a mechanism for overcharging
NaNiCl2 | 78% - 85 % | + | - | -- | + | o | High operating temperature (300 °C)
Lithium-ion battery meets the criteria for this application best
[1] Soloveichik, Grigorii L.. “Battery technologies for large-scale stationary energy storage.” Annual review of chemical and biomolecular engineering 2 (2011): 503-27
[2] https://www.sciencedirect.com/topics/earth-and-planetary-sciences/nickel-cadmium-battery#:~:text=NiCd%20batteries%20cool%20as%20they,have%20claimed%20up%20to%2085%25.
[3] https://www.sciencedirect.com/topics/engineering/ah-efficiency#:~:text=Lead%E2%80%93acid%20batteries%20typically%20have,the%20higher%20is%20the%20efficiency

## Slide 9: Battery Cell
Source:...
Capacity | 
Rated Voltage | 
Charge cut-off voltage | 
Discharge cut-off voltage | 
Shape (diameter x length) | 
Charge/discharge cycles (25°C, 1C) | 
Operating temperature | 
Weight | 
Short-term max. current (10s) | 
Continuous discharge current | 
Continuous charge current | 
Price per cell | 

## Slide 10: Battery Pack Design
Efficiency (Battery to Wheel) |  | 
Electric power needed from the battery |  | 
Short term maximum power per cell (10s) |  | 
Least number of cells needed |  | 
Selected number of cells |  | 
Total battery capacity |  | 
Price for the cells |  | 
Weight for cells |  | 
Weight for the battery system | [1] | 
Volume of battery system | [1] | 
Continuous power (charging ¦ discharging) |  | kW ¦ kW
Efficiency (Battery to Wheel) |  | 
Electric power needed from the battery |  | 
Short term maximum power per cell (10s) |  | 
Least number of cells needed |  | 
Selected number of cells |  | 
Total battery capacity |  | 
Price for the cells |  | 
Weight for cells |  | 
Weight for the battery system |  | 
Volume of battery system |  | 
Continuous power (charging ¦ discharging) |  | 
1:Hendrik Löbberding, Saskia Wessel, Christian Offermanns, Mario Kehrer, Johannes Rother, Heiner Heimes and Achim Kampker; From Cell to Battery System in BEVs: Analysis of System Packing Efficiency and Cell Types; World Electric Vehicle Journal 2020, 11, 77; doi:10.3390/wevj11040077

## Slide 11: Topology Selection
Cells are connected in series in our battery pack design
  Nominal voltage: 240 V
Criteria for selection of this topology
  Typical voltage level of Hybrid vehicles are 200-400V[1]
  Parallel or modular connection of the same voltage would result in a much larger energy capacity than required, making it economically worse and increasing the weight
  Less complex BMS required
Problem with the selected topology
  Low reliability – worst cell limits the lifetime
  Less control over each section than modular
Source: pveducation.org
1: Budde-Meiwes, Heide & Drillkens, Julia & Lunz, Benedikt & Muennix, Jens & Lehner (maiden name Rothgang), Susanne & Kowal, Julia & Sauer, Dirk. (2013). A review of current automotive battery technology and future prospects. Proceedings of the Institution of Mechanical Engineers, Part D: Journal of Automobile Engineering. 227. 761-776. 10.1177/0954407013485567

## Slide 12: Battery Management System
Functions:
  Monitoring
    Voltage, current, temperature
  Protection
    Against undervoltage
    Too high current
    Fixed temperature limit: 60°C
  Charging and discharging Management
    Balance SOC of the cells
  Communication
    With vehicle control unit
  Diagnosis
    SOH, total number of cycles
Requirements:
  Avoid Electromagnetic Interference (EMI)
  Contactors
  Redundancy
  Galvanic Isolation
Source: mdpi.com

## Slide 13: Battery Management System
Centralized topology
  Single master module is connected to the cells serially
  Advantages:
    Cheap
    Less maintenance
    Good accuracy
  Disadvantages:
    Limited scalability and flexibility
    Less reliability
Thermal Management Module
Balancing Control Mode
High Voltage Safety Control
Communication Module
General Digital Outputs
Global Clock Module
Man-machine interface Module
General Digital Inputs
General Analogue Inputs
Cell Voltage Measurement
Temperature Sensor Array
Bus Voltage/ Current Measurement
Charging System
Internal Power Supply Module
Source: lithiumbalance.com
Source: Characteristics of Battery Management Systems of Electric Vehicles with Consideration of the Active and Passive Cell Balancing Process. Muhammad Uzair, Ghulam Abbas and Saleh Hosain

## Slide 14: Cooling system
Active air cooling
Keeping battery between 20 - 40ºC
Shared use of passenger compartment air conditioning
The system has a fan activated by the battery control unit
Four temperature sensors:
  one in the air intake area and the other three along the battery module
Ventilation inlets near the rear seats and outlet in the car boot
Low weight
Source: autofacil.com

## Slide 15: Cooling system
Heat spreaders:
  Graphite sheets coated with thin dielectric films or thermally conductive metal foils
  Flexible heat spreaders can weave between cells before terminating at heat sinks
Heat sink with a high level of thermal conductivity:
  aluminium, copper, etc.
Homogeneous temperature distribution
  Temperature gradient less than 5ºC
Energy efficient
Low cost
Source: edn.com

## Slide 16: Load Profile Estimation
Use velocity and acceleration of WLTP cycles
Distance: 23.3 km, duration: 30 min
Calculate the energy needed for every 1-second-interval
Calculate the SOC of the battery during the cycle
Drive electric under 38 km/h
Properties of the Toyota C-HR used
Source: csm.de
Source: Toyota

## Slide 17: Load Profile Estimation – Power
Average power: 10.9 kW (7.6 C at 2.4 V - 9.1 C at 2.0 V)

## Slide 18: Load Profile Estimation – SOC
Average DOD per cycle: 3 % (= 43.2 Wh)
Total amount of energy charged/discharged: 0.65 kWh
Assume 15 cycles of 3 % DOD during a 23.3 km drive
Fuel savings: 20.6 % (from 6.2 l/100km to 4.9 l/100km)
In city driving conditions a fuel reduction of 41.7 % is possible
0
100
Duration
SOC[%]

## Slide 19: Cyclic Ageing Estimation
Average DOD of 3% per cycle
From the Wöhler curve it yields 106 cycles
From Load profile, 15 cycles per 23.3 km
Total driving distance of 1 553 333 km in its cycle lifetime
Inaccuracy in our assumption
  The curve is for conventional Li-ion batteries, LTO's have better cycle life
  In the curve C rate is 1 whereas average C rate is 9C
  Variance in cell quality would affect ageing
  Effect of calendric ageing on cyclic ageing not considered
Cyclic Life Tests
  Varying DOD, C rate and Temperature
Source: Encyclopedia of Electrochemical Power Sources, Editor-in-Chief Jürgen Garche, Elsevier, 2009, page 522-538
Lifetime prediction Dirk Uwe Sauer a, Heinz Wenzl b

## Slide 20: Calendric Ageing Estimation
Assumption of the resting SOC is 50%
Assumed temperature is 25° C
SOH drops 3% in 21 months
With extrapolation, SOH of battery would drop below 80% after 140 months or 12 years
Inaccuracy in our assumption:
  Resting SOC would vary
  Variance in Temperature is not considered
  The curve is for conventional Li-ion batteries
  Calendric ageing would be affected by variance of cell quality as well
Calendric Life Tests
  Varying SOC and Temperature
Source: Effects of Biphenyl Polymerization on Lithium Deposition in Commercial Graphite/NMC Lithium-Ion Pouch-Cells during Calendar Aging at High Temperature
Bramy Pilipili Matadi,a,b Sylvie Geni`es,c,d Arnaud Delaille,a,b,zThomas Waldmann,e Michael Kasper,eMargret Wohlfahrt-Mehrens,eFrederic Aguesse,fEmilie Bekaert,f
Isabel Jim´enez-Gordon,c,d Lise Daniel,c,d Xavier Fleury,c,d Michel Bardet,g Jean-Fr´ed´ eric Martin,c,d and Yann Bultelh,

## Slide 21: Cost Analysis
Hybrid car components
  Battery
  Cooling system
  Power Electronics
  BMS-System
  Safety components
  Electric motor
Total costs: 5000 € [1,2]
Break-Even-Point:
  Gasoline price: 1.70 € per liter
  20.6%: (231 000 km, 24 340 €)
  41.7%: (114 000 km, 12 010 €)
1:https://www.greengear.de/hybridantrieb-paralleler-hybrid/
2:https://www.toyota.de/download/cms/dede/P50826_Toyota_Edition-S_SoMo_Web_tcm-17-694546.pdf

## Slide 22: Conclusion
High power Li-Ion Battery (LTO)
Connected in series for high voltage
Sufficient to power the electric motor at maximum power for 10s
Can provide 14.4 kW (charging) / 28.8 kW (discharging) continuously
Active air cooling
Lifetime: 1.55 Mio km or 12 years
Fuel savings 20.6 % (in city driving conditions 41.7%)
Total extra cost for the hybrid system 5000 € (1800€ for the cells only)
After 230 000 km it will be cheaper than a conventional car

## Slide 23: Full hybrid vehicle with an electric machine of 70 kW motor power
Battery Storage Systems WS 21/22

## Slide 24: Backup - Load Profile Estimation
For every 1-second-interval
coefficient | value
mass | 1460kg 1
Cw value | 0.31 2
area | 2.45 2
Rolling resistance factor | 0.013 3
velocity
acceleration
intertial force
power
*v
energy
drag force
rol. res. force
15% losses
15% losses
Regenerative breaking: E < 0
Electric driving: v < 38
Combustion driving: v > 38
SOC
fuel consumption
*1s
1toyota.de
2 automobil-guru.de
3engineeringtoolbox.com

## Slide 25: Backup - Load Profile Estimation
Second Scenario: low and medium speed – now drive electric up to 32 km/h
Assume 16.8 cycles of 3 % DOD during a 15.7 km drive
Fuel savings: 41.7 %

## Slide 26: Backup - Tank-to-wheel efficiency
Odd André Hjelkrem, Petter Arnesen, Torstein Aarseth Bø, Rebecka Snefuglli Sondell,
Estimation of tank-to-wheel efficiency functions based on type approval data,
Applied Energy, Volume 276, 2020
https://doi.org/10.1016/j.apenergy.2020.115463

## Slide 27: Backup - Battery Technologies – Power Density
Technology | Gravemetric Energy Density | Gravemetric Power Density
Lead-acid (Pb) | -- | -
Nickel-cadmium (NiCd) | - | o
Nickel-metal hydride (NiMH) | o | +
Lithium-ion (Li-ion) | ++ | ++
Sodium-nickel chloride (NaNiCl2) | + | --
Gravimetric Energy-and Power Density1
: Considered Point for this application:
1: Budde-Meiwes, Heide & Drillkens, Julia & Lunz, Benedikt & Muennix, Jens & Lehner (maiden name Rothgang), Susanne & Kowal, Julia & Sauer, Dirk. (2013). A review of current automotive battery technology and future prospects. Proceedings of the Institution of Mechanical Engineers, Part D: Journal of Automobile Engineering. 227. 761-776. 10.1177/0954407013485567